## Slide 1: Bio Image Analysis
Christian Tischer
Advanced Light Microscopy Facility (Rainer Pepperkok)
EMBL Heidelberg
tischitischer@gmail.com

## Slide 2: Menu
This Lecture:
  Image analysis methods that I typically need to help people at our institute
Today’s Practical:
  Using ImageJ
  How to inspect my data and judge its quality
  Conducting object-based measurements
Project (Sat&Sun):
  Become an ImageJ expert
  Apply most of the methods that I present today
  Learn some programming to automate your analyses

## Slide 3: Bioimage Analysis
Sample preparation
Microscopy
Image analysis
QC & Statistics
Biological question
1. Acquire only few images of controls.
2. Establish your analysis workflow.
3. Acquire more data.

## Slide 4: Image Analysis Software @ EMBL Heidelberg
Free, open-source
  Fiji/ImageJ (2-D & 3-D)
  CellProfiler (2-D batch analysis)
  Ilastik (2-D & 3-D, supervised pixel classification)
  CellCognition (2-D, supervised object classification)
  Python
  R
Commerical
  Matlab
  Imaris (3-D)
  Volocity (3-D)

## Slide 5: An image is a matrix of numbers
8-bit: 0,1,..,255 (2^8-1)
12-bit: 0,1,..,4095 (2^12-1) 
16-bit: 0,1,..,65535 (2^16-1)
Lookup Table (LUT)
“Grays”
“Green”
“Fire”

## Slide 6: Object detection (segmentation)

## Slide 7: 1. Intensity threshold (“binarize”) 2. Object detection (“connected components”) 3. Object filtering, based on location and shape
Fiji: Image..Adjust..Threshold; Analyze..Analyze Particles
CellProfiler: IdentifyPrimaryObjects
Finding the threshold:
Manual
Various automated methods
Threshold
Gray value histogram

## Slide 8: Signal to Noise (S/N)
S/N = (Mean(Object)- Mean(BG)) / SD(BG)
  Important for (automated) object detection
  Important for intensity measurements
S/B = Mean(Object) / Mean(BG)
  Important for ?
Signal
Noise
Background
Signal
BG Noise

## Slide 9
Intensity threshold
Raw data
“Enhance” raw data
Objects

## Slide 10: Morphological tophat filter removes local background
raw
erosion (r=7)
dilation (erosion, r=7)
tophat = raw - dil(ero(raw))
top-hat & threshold
raw & threshold

## Slide 11
Intensity threshold
Raw data
“Enhance” raw data
Objects
Tophat
Difference of Gaussian
Edge enhancements
Local texture
Many, many more……

## Slide 12: Supervised pixel classification
Fiji/ImageJ:
Trainable Weka Segmentation
www.ilastik.org
Label different image regions.
Software computes many different filters on the image.
Based on your labels it learns which filters distinguish the different regions best.
Lung sections with tumors, Hematoxylin & Eosin stain
Martina Mantovan, EMBL Monterodondo

## Slide 13: Object (region) growing

## Slide 14: Distance-based region growing (“dilation”)
Simple and robust, not very accurate
HeLa Kyoto cells, stained with HCS CellMask (Lifetechnologies)

## Slide 15
Object growing that stops when
(i) signal drops below threshold or (ii) runs into another region
You need a cytoplasm staining for this
You have to set a background threshold (to stop region growing)
Not accurate at cell-cell contacts

## Slide 16
Image-based watershed to find cell-cell contacts
Inverted
Nuc1
Nuc2
Raw data
Nuc1
Nuc2
Fiji: Process..Find Maxima (Output type: segmented particles
CP: IndentifySecondaryObjects (Watershed - Image)

## Slide 17: Recommendation for tissue culture cell detection: Nucleus stain & Whole cell stain Use nuclei as seeds for image-based watershed

## Slide 18: Object splitting

## Slide 19: Shape-based object splitting by watershed filter on distance transform

## Slide 20: Object Measurements

## Slide 21: How would you measure the difference between these nuclei?

## Slide 22: Area

## Slide 23: Mean intensity

## Slide 24: Mean vs. Sum Intensities
Gray values: 105, 133, 148, 142
Sum = 105 + 133 + 148 + 142 = 528
Area (in pixels) = 4
Mean = Sum / PixelArea = 132
Sum = Mean * PixelArea
ImageJ:
[Image > Properties]; [Analyze > Measure]
Sum ~ Total amount
Mean ~ Concentration

## Slide 25
Form-factor = 4*π*Area / Perimeter^2
Circle: P = 2*π*R; A = π*R^2; FF = 4*π*π *R^2 / (2*π*R)^2 =
4*π^2*R^2 / (4*π^2*R^2) = 1
Line: FF = 4*π*L / L^2 = 4*π / L
(small for long lines)

## Slide 26: Haralick texture features
H1: Angular Second Moment
H2: Contrast
H3: Correlation
H4: Sum of Squares: Variation
H5: Inverse Difference Moment
H6: Sum Average
H7: Sum Variance
H8: Sum Entropy
H9: Entropy
H10: Difference Variance
H11: Difference Entropy
H12: Information Measure of Correlation 1
H13: Information Measure of Correlation 2
Haralick et al. (1973), "Textural Features for Image Classification," IEEE Transaction on Systems Man, Cybernetics, SMC-3(6):610-621.

## Slide 27: Many features to distinguish phenotypes… which ones to choose?

## Slide 28: Supervised object classification
(200, 0.5, 0.4, 0.33, …)
“Feature vector” = (area, form factor, mean intensity, H1, …)
(400, 0.8, 0.3, 0.12, …)
(410, 0.85, 0.29, 0.54, …)
(440, 0.84, 0.3, 0.60, …)
(350, 0.75, 0.2, 0.55 …)
?
Algorithms that predict unknown vectors based on known ones:
“Support Vector Machines”
“Random Forests”

## Slide 29: www.cellcognition.org

## Slide 30: Intensity measurements

## Slide 31: The meaning of intensities: widefield vs. confocal images

## Slide 32: Confocal: optical sectioning (60x NA1.4 Airy1)
Chart: z-position [micrometer]
| -11.25 | -10.0 | -8.75 | -7.5 | -6.25 | -5.0 | -3.75 | -2.5 | -1.25 | 0.0 | 1.25 | 2.5 | 3.75 | 5.0 | 6.25 | 7.5 | 8.75 | 10.0 | 11.25 | 12.5
 | 9031.007 | 10268.3705 | 12240.6285 | 16390.7 | 25625.919 | 45363.2775 | 98978.332 | 188709.3535 | 267858.969 | 291687.285 | 321612.404 | 275648.582 | 136471.3865 | 34882.634 | 14806.7135 | 9600.651 | 7351.632 | 5523.1285 | 4575.961 | 3619.389
0
100

## Slide 33: Widefield (20x NA0.7) selective focus but no optical sectioning
Chart: z-position [micrometer]
| -16.0 | -14.0 | -12.0 | -10.0 | -8.0 | -6.0 | -4.0 | -2.0 | 0.0 | 2.0 | 4.0 | 6.0 | 8.0 | 10.0 | 12.0 | 14.0
 | 1336277.6427 | 1341897.8391 | 1345975.5556 | 1351111.1276 | 1357427.5195 | 1362662.548 | 1370156.1432 | 1371794.463 | 1377640.6969 | 1382808.8183 | 1385770.8137 | 1390683.9648 | 1390772.5715 | 1392817.7588 | 1393463.3219 | 1390738.2138

## Slide 34: Widefield vs. confocal
Wide-field is good for measuring the total amount of a protein in thin samples (e.g., tissue culture cells).
Confocal microscopy is good for measuring local protein concentrations and for thick 3-D samples.

## Slide 35: Intensity measurements require background subtraction
Select a proper BG ROI
Measure mean intensity in the BG ROI
Subtract the measured value from all pixels in the image
Increase brightness & contrast!

## Slide 36
z
z-slice middle of cell
z-slice bottom of cell
y
x
y
x
Thanks to Yin Cai for the data
You have to consider the shape of the PSF !
Interpretation of intensities in confocal images

## Slide 37: Interpretation of intensities in confocal images
z

## Slide 38: 3-D projections
Statistics, e.g.
Mean
Max
Sum
SD
…
z-stack
Protein in dividing HeLa cell, data from Yin Cai @ EMBL, Heidelberg
z-max projection

## Slide 39: Properties of sum and maximum projections
Sum projection
y
x
z
Max projection
*
*
Sum projection:
  good for whole cell quantification ~ total amount of protein (if you imaged the whole cell)
Max. projection:
  good to find objects (and measure their intensity)
*
*
*
*
Sum projection
*
*
Max projection

## Slide 40: Automated Filtering (Quality Control, QC)

## Slide 41: Automated cell-based QC
Mean intensity < 0.4
CellProfiler: FilterObjects
Fiji: Analyze.Analyze Particles
Typical cell QCs:
Abnormal (nucleus) morphology
Contains saturated pixels
Expression level too low or too high
HeLa Kyoto cells
nucleus and autophagosomes
(Kenta Imai)

## Slide 42: Automated Image QC
Measurement: Focus quality (“PowerLogLogSlope”) from CellProfiler module MeasureImageQuality
-2.0
-3.1
Typical image QCs:
Focus quality
Background intensity
Number of cells

## Slide 43: Automated image analysis
Correct?
Significant?
Many images
Many numbers
Image analysis

## Slide 44: Categorical Plots
[1] "Control mean = 7.24 sd = 4.55"
[1] "BFA t-test vs. Control = 2.73e-06 (**)"
[1] "Nocodazole t-test vs. Control = 3.72e-20 (**)"
+
+

## Slide 45: Heatmaps
Blue = little actin ruffling
Red = much actin ruffling

## Slide 46: You need a convenient* way to link back the numbers to the images!
*(otherwise you might not do it)

## Slide 47: Thank you for your attention!
Thanks for discussions or slides:
Antonio Politi (EMBL HD)
Kota Miura (EMBL HD)
Malte Wachsmuth (EMBL HD)
Thanks for sharing data:
Yin Cai (EMBL HD)
Anita Ripplinger (University of Copenhagen)

## Slide 48: Data organisation

## Slide 49: Structure your data and give it computer-readable names
“Assay1 Rep 2014,03,20 Control 1.tif”
“Assay1 Replicate 2014,03,20 Control 10.tif”
“HeLa_Endocytosis--2014-03-20--NegCtrl--001.tif”
“HeLa_Endocytosis--2014-03-20--NegCtrl--002.tif”
“HeLa_Endocytosis--2014-03-20--PosCtrl--001.tif”
“HeLa_Endocytosis--2014-03-20--TreatA--001.tif”
“HeLa_Endocytosis--2014-04-01--NegCtrl--001.tif”
“HeLa_Endocytosis--2014-04-01--TreatA--001.tif”
BiologicalAssay--ExperimentalBatch--Treatment--ID

## Slide 50: QC on automated background measurement
Typical image QCs:
Focus quality
Background intensity
Cell density
*
*
*

## Slide 51: Background subtraction

## Slide 52: Selecting the right background ROI
Increase brightness & contrast!

## Slide 53: Background subtraction issue: dense cells
If there is no clear background region you have a problem…
Solutions:
  Seed your cells less dense
  Select image fields with clear background
  Measure the background in another (neighboring) image

## Slide 54: Statistics  Automated analysis…
Find damage sites (auto threshold the protein Ctrl image)
Use damage sites as “seeds” and “dilate” to find rest of cell (automated “region growing”)
Measure sum signal in cell ROIs in background corrected image (background subtraction on whole image)
Measure sum signal in damage ROIs in top-hat filtered image
Compute the ratios…
www.cellprofiler.org
“Signal in damage region”
= Sum(Cut)–Mean(CutNH)*Area(Cut)
= Sum(Cut) if Mean(CutNH)=0

## Slide 55: Local background subtraction by top-hat filtering
Chart: Intensity line profiles
raw
min(raw, r=15)
max(min(raw), r=15)
tophat =
raw-max(min(raw,r=15)

## Slide 56: Background subtraction

## Slide 57: Manual background measurement
Carefully select background ROI (increase brightness to see “dirt” and dim cells)
Measure median intensity
The resulting image should support negative numbers
  Fiji: Image..Type..32-bit; Process..Math..Subtract

## Slide 58: Automated background measurement: Measure intensity outside objects
Each image has its own background measured
Fails if cells are too dense…
*
*
*

## Slide 59: Background subtraction for small isolated structures: Top-hat filtering
Chart: Intensity line profiles
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0 | 51.0 | 52.0
raw | 19 | 18.3379 | 19.6569 | 20.8803 | 21.401 | 21.5415 | 35.6097 | 41.9474 | 66.1741 | 79.9912 | 100.5032 | 101.5476 | 84.9656 | 66.5125 | 60.4464 | 52.2686 | 58.4542 | 74.5457 | 80.414 | 71.6116 | 66.2425 | 52.8026 | 41.107 | 40.9205 | 41.3776 | 37.6725 | 37.4462 | 38.8066 | 41.0975 | 44.5978 | 41.0532 | 35.2313 | 30.2264 | 32.5006 | 30.5827 | 29.6284 | 32.9809 | 38.3292 | 42.6423 | 52.0482 | 65.8675 | 62.7633 | 52.6136 | 36.0164 | 25.4751 | 22.6576 | 19.7912 | 19.2669 | 18.7474 | 18.3023 | 17.703 | 18.0333 | 19.706
erode | 10 | 10 | 10.6529 | 10.9799 | 11 | 11 | 12.8367 | 13 | 13.6103 | 13.9413 | 14 | 14 | 14 | 16.254 | 18.3725 | 23.3953 | 27.7555 | 31 | 30.8633 | 29.6533 | 27.4878 | 27.0043 | 27 | 24.6411 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 21.7203 | 18.3569 | 16 | 15.9711 | 11.5471 | 8.6768 | 7.9685 | 7 | 7 | 7 | 7.486 | 7.2757 | 10.0502 | 10.0498 | 10 | 10 | 10.588
dilate(erode) | 15 | 16.6485 | 16.9821 | 17.4861 | 20.1791 | 21.5052 | 32.8671 | 33.9426 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 33.5994 | 33.7419 | 33.8791 | 34 | 33.8122 | 33.5365 | 33.9177 | 33.4705 | 33.0233 | 31.1109 | 27.7672 | 24.3797 | 23.5934 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 21.7999 | 21 | 19.6516 | 16.9748 | 15.9469 | 15.0525 | 12.4743 | 12 | 12
top-hat | 4 | 1.6895 | 2.6748 | 3.3942 | 1.2218 | 0.0363 | 2.7426 | 8.0049 | 32.1741 | 45.9912 | 66.5032 | 67.5476 | 50.9656 | 32.5125 | 26.4464 | 18.2686 | 24.4542 | 40.5457 | 46.414 | 37.6116 | 32.2425 | 18.8026 | 7.5076 | 7.1786 | 7.4985 | 3.6725 | 3.634 | 5.2701 | 7.1797 | 11.1273 | 8.0298 | 4.1204 | 2.4592 | 8.1209 | 6.9893 | 6.6284 | 9.9809 | 15.3292 | 19.6423 | 29.0482 | 42.8675 | 39.7633 | 29.6136 | 13.0164 | 3.6752 | 1.6576 | 0.1396 | 2.2921 | 2.8004 | 3.2498 | 5.2287 | 6.0333 | 7.706

## Slide 60: Quantitative intensity measurements are not possible with saturation
Chart: distance
Signs of saturation:
Areas with exactly same high intensity (line-profile)
Intensity values at the end of bit depths: 255 (8 bit); 4095 (12 bit); 16383 (14 bit); 65535 (16 bit)
Check at microscope and adapt excitation and signal amplification such that no sample is overexposed (can be tricky if you have many samples…)

## Slide 61: Quantitative intensity measurements
Only meaningful in comparison => you need controls (measured with same settings in same microscopy session)
Saturated pixels cannot be quantified
You need to properly subtract the image background
NEVER save your images in a different format or convert the bit-depth, unless you KNOW EXACTLY what you are doing
Be aware about the different biological interpretations of mean vs. sum intensities in confocal vs. widefield imaging

## Slide 62
Thank you for your attention!

## Slide 63: What to measure, exactly?

## Slide 64: “Actin ruffling” in siRNA knockdown conditions
number of ruffle pixels per image
number of ruffle pixels per cell
ruffles pixels per cell / cell area
integrated intensity in ruffle area
integrated intensity in ruffle area / integrated intensity in whole cell
mean intensity in ruffle area
…
Mouse Embryonic Fibroblasts
stimulated with PDGF 20 ng/ml for 10 min
Salvatore Corallino, IFOM, Milan
Let’s say you managed to detect the ruffle pixels;
What would you measure?

## Slide 66
Chart: Intensity line profiles
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0 | 51.0 | 52.0
raw | 19 | 18.3379 | 19.6569 | 20.8803 | 21.401 | 21.5415 | 35.6097 | 41.9474 | 66.1741 | 79.9912 | 100.5032 | 101.5476 | 84.9656 | 66.5125 | 60.4464 | 52.2686 | 58.4542 | 74.5457 | 80.414 | 71.6116 | 66.2425 | 52.8026 | 41.107 | 40.9205 | 41.3776 | 37.6725 | 37.4462 | 38.8066 | 41.0975 | 44.5978 | 41.0532 | 35.2313 | 30.2264 | 32.5006 | 30.5827 | 29.6284 | 32.9809 | 38.3292 | 42.6423 | 52.0482 | 65.8675 | 62.7633 | 52.6136 | 36.0164 | 25.4751 | 22.6576 | 19.7912 | 19.2669 | 18.7474 | 18.3023 | 17.703 | 18.0333 | 19.706
erode | 10 | 10 | 10.6529 | 10.9799 | 11 | 11 | 12.8367 | 13 | 13.6103 | 13.9413 | 14 | 14 | 14 | 16.254 | 18.3725 | 23.3953 | 27.7555 | 31 | 30.8633 | 29.6533 | 27.4878 | 27.0043 | 27 | 24.6411 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 21.7203 | 18.3569 | 16 | 15.9711 | 11.5471 | 8.6768 | 7.9685 | 7 | 7 | 7 | 7.486 | 7.2757 | 10.0502 | 10.0498 | 10 | 10 | 10.588
dilate(erode) | 15 | 16.6485 | 16.9821 | 17.4861 | 20.1791 | 21.5052 | 32.8671 | 33.9426 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 34 | 33.5994 | 33.7419 | 33.8791 | 34 | 33.8122 | 33.5365 | 33.9177 | 33.4705 | 33.0233 | 31.1109 | 27.7672 | 24.3797 | 23.5934 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 23 | 21.7999 | 21 | 19.6516 | 16.9748 | 15.9469 | 15.0525 | 12.4743 | 12 | 12
top-hat | 4 | 1.6895 | 2.6748 | 3.3942 | 1.2218 | 0.0363 | 2.7426 | 8.0049 | 32.1741 | 45.9912 | 66.5032 | 67.5476 | 50.9656 | 32.5125 | 26.4464 | 18.2686 | 24.4542 | 40.5457 | 46.414 | 37.6116 | 32.2425 | 18.8026 | 7.5076 | 7.1786 | 7.4985 | 3.6725 | 3.634 | 5.2701 | 7.1797 | 11.1273 | 8.0298 | 4.1204 | 2.4592 | 8.1209 | 6.9893 | 6.6284 | 9.9809 | 15.3292 | 19.6423 | 29.0482 | 42.8675 | 39.7633 | 29.6136 | 13.0164 | 3.6752 | 1.6576 | 0.1396 | 2.2921 | 2.8004 | 3.2498 | 5.2287 | 6.0333 | 7.706

## Slide 67
Difference of Gaussian Filter

## Slide 68
Small Gaussian blur
Large Gaussian blur
Difference of Gaussian
Difference of Gaussian & Threshold

## Slide 69: Difference of Gaussian vs. Top-hat …
Difference of Gaussian filtering:
  Inherently smoothens the image
  Enhances spots but also edges
Top-hat filtering:
  Sensitive to noise
  Does not enhance edges
Filter X:
  …..
Filter Y:
….

## Slide 70: Statistical Analysis..…

## Slide 71: How many images do I need?
Mean
  Property of your assay and the biology
  More experiments => your estimation of the mean is more precise
Standard deviation (SD)
  Property of your assay and the biology
  More experiments => your estimation of the standard deviation is more precise (put the error formula)
Standard error of the mean (SEM)
  SD/(Sqrt(NumberOfExperiments)-1)
  More experiments => the SEM decreases <=> you know more precisely what the mean is

## Slide 72: Stuff

## Slide 73: distance transform

## Slide 74: distance-transform region growing (watershed)

## Slide 75: Local intensity thresholding
issues: inhomogeneous background (such as cellular cytoplasm)
Niblack
Implements Niblack's thresholding method:
pixel = ( pixel > mean + k * standard_deviation - c) ? object : background
Parameter 1: is the k value. The default value is 0.2 for bright objects and -0.2 for dark objects. Any other number than 0 will change the default value.
Parameter 2: is the C value. This is an offset with a default value of 0. Any other number than 0 will change its value. This parameter was added in version 1.3 and is not part of the original implementation of the algorithm. The original algorithm is applied when C = 0.
Niblack, W (1986), An introduction to Digital Image Processing, Prentice-Hall
Ported from ME Celebi's fourier_0.8 routines [3] and [4].
ImageJ:
Image..Adjust..Auto Local Threshold
CellProfiler:
try with cellprofiler (latest version on my mac)

## Slide 76: Enhancement of locally bright structures by top-hat filtering
…
Chart: 
| 0.0 | 3.22000000000001E-5 | 6.44000000000003E-5 | 9.66000000000004E-5 | 0.0001288 | 0.000161 | 0.000193200000000001 | 0.0002254 | 0.0002576 | 0.0002898 | 0.000322000000000001 | 0.000354200000000001 | 0.000386400000000001 | 0.0004186 | 0.000450800000000001 | 0.000483000000000001 | 0.0005152 | 0.000547400000000001 | 0.000579600000000001 | 0.0006118 | 0.000644000000000002 | 0.000676200000000001 | 0.000708400000000001 | 0.000740600000000002 | 0.000772800000000001 | 0.000805000000000002 | 0.000837200000000004 | 0.0008694 | 0.000901600000000002 | 0.0009338 | 0.000966000000000002 | 0.000998200000000004 | 0.0010304 | 0.0010626 | 0.0010948 | 0.001127 | 0.0011592 | 0.0011914 | 0.0012236
 | 12.9142 | 15.9707 | 17.6876 | 18.1955 | 17.9797 | 15.3479 | 17.0815 | 18.2693 | 20.0872 | 19.6819 | 17.6555 | 27.1179 | 31.7175 | 37.9065 | 38.9139 | 40.2006 | 41.6515 | 53.3277 | 67.6913 | 58.5348 | 43.3792 | 36.2151 | 41.3582 | 35.2458 | 28.0703 | 28.5157 | 24.7911 | 19.4222 | 13.7273 | 16.9442 | 18.1036 | 21.6951 | 14.5257 | 12.8757 | 11.6201 | 9.6155 | 10.8317 | 13.9311 | 15.7572
 | 9 | 9.4991 | 10.8255 | 11.6604 | 12.3255 | 12.7869 | 13 | 13 | 13 | 12.9572 | 13 | 13 | 13.272 | 17.3028 | 23.6286 | 28.2961 | 29.9101 | 31.7497 | 31.895 | 31.9836 | 31.0604 | 27.984 | 26.2034 | 24.0906 | 20.0234 | 14.2051 | 11.2048 | 10.9956 | 10.3695 | 10.2495 | 9.5231 | 9.3242 | 6.7474 | 6 | 6 | 6 | 6 | 6.1329 | 8.069
 | 11.6464 | 12.2494 | 12.8702 | 13 | 13 | 13 | 13.0901 | 13.0275 | 13.3237 | 13.4015 | 15.7295 | 22.7849 | 28.1693 | 30.5919 | 31.8826 | 32.321 | 33 | 33 | 33.6198 | 33.5686 | 34.3932 | 34.5431 | 33.5793 | 31.9374 | 28.0306 | 27.3291 | 23.6428 | 19.1722 | 13.3026 | 11.7422 | 11.0285 | 11 | 11 | 10.9545 | 9.8982 | 7.9771 | 9.2768 | 9.9512 | 10
 | 1.2678 | 3.7213 | 4.8174 | 5.1955 | 4.9797 | 2.3479 | 3.9914 | 5.2419 | 6.7634 | 6.2805 | 1.9261 | 4.333 | 3.5481 | 7.3146 | 7.0313 | 7.8797 | 8.6515 | 20.3277 | 34.0715 | 24.9662 | 8.986 | 1.6721 | 7.7789 | 3.3084 | 0.039759 | 1.1866 | 1.1483 | 0.25 | 0.4247 | 5.202 | 7.0752 | 10.6951 | 3.5257 | 1.9212 | 1.7219 | 1.6384 | 1.555 | 3.98 | 5.7572

## Slide 77: Enhancement of locally bright structures by top-hat filtering
…
Chart: 
| 0.0 | 3.22000000000001E-5 | 6.44000000000003E-5 | 9.66000000000004E-5 | 0.0001288 | 0.000161 | 0.000193200000000001 | 0.0002254 | 0.0002576 | 0.0002898 | 0.000322000000000001 | 0.000354200000000001 | 0.000386400000000001 | 0.0004186 | 0.000450800000000001 | 0.000483000000000001 | 0.0005152 | 0.000547400000000001 | 0.000579600000000001 | 0.0006118 | 0.000644000000000002 | 0.000676200000000001 | 0.000708400000000001 | 0.000740600000000002 | 0.000772800000000001 | 0.000805000000000002 | 0.000837200000000004 | 0.0008694 | 0.000901600000000002 | 0.0009338 | 0.000966000000000002 | 0.000998200000000004 | 0.0010304 | 0.0010626 | 0.0010948 | 0.001127 | 0.0011592 | 0.0011914 | 0.0012236
 | 12.9142 | 15.9707 | 17.6876 | 18.1955 | 17.9797 | 15.3479 | 17.0815 | 18.2693 | 20.0872 | 19.6819 | 17.6555 | 27.1179 | 31.7175 | 37.9065 | 38.9139 | 40.2006 | 41.6515 | 53.3277 | 67.6913 | 58.5348 | 43.3792 | 36.2151 | 41.3582 | 35.2458 | 28.0703 | 28.5157 | 24.7911 | 19.4222 | 13.7273 | 16.9442 | 18.1036 | 21.6951 | 14.5257 | 12.8757 | 11.6201 | 9.6155 | 10.8317 | 13.9311 | 15.7572
 | 9 | 9.4991 | 10.8255 | 11.6604 | 12.3255 | 12.7869 | 13 | 13 | 13 | 12.9572 | 13 | 13 | 13.272 | 17.3028 | 23.6286 | 28.2961 | 29.9101 | 31.7497 | 31.895 | 31.9836 | 31.0604 | 27.984 | 26.2034 | 24.0906 | 20.0234 | 14.2051 | 11.2048 | 10.9956 | 10.3695 | 10.2495 | 9.5231 | 9.3242 | 6.7474 | 6 | 6 | 6 | 6 | 6.1329 | 8.069
 | 11.6464 | 12.2494 | 12.8702 | 13 | 13 | 13 | 13.0901 | 13.0275 | 13.3237 | 13.4015 | 15.7295 | 22.7849 | 28.1693 | 30.5919 | 31.8826 | 32.321 | 33 | 33 | 33.6198 | 33.5686 | 34.3932 | 34.5431 | 33.5793 | 31.9374 | 28.0306 | 27.3291 | 23.6428 | 19.1722 | 13.3026 | 11.7422 | 11.0285 | 11 | 11 | 10.9545 | 9.8982 | 7.9771 | 9.2768 | 9.9512 | 10
 | 1.2678 | 3.7213 | 4.8174 | 5.1955 | 4.9797 | 2.3479 | 3.9914 | 5.2419 | 6.7634 | 6.2805 | 1.9261 | 4.333 | 3.5481 | 7.3146 | 7.0313 | 7.8797 | 8.6515 | 20.3277 | 34.0715 | 24.9662 | 8.986 | 1.6721 | 7.7789 | 3.3084 | 0.039759 | 1.1866 | 1.1483 | 0.25 | 0.4247 | 5.202 | 7.0752 | 10.6951 | 3.5257 | 1.9212 | 1.7219 | 1.6384 | 1.555 | 3.98 | 5.7572

## Slide 78: gradient-based region growing (watershed)

## Slide 79: Standard deviation of intensity

## Slide 80: widefield microscopy is the best method to measure total protein levels in tissue culture cells
Chart: z-position [micrometer]
| -16.0 | -14.0 | -12.0 | -10.0 | -8.0 | -6.0 | -4.0 | -2.0 | 0.0 | 2.0 | 4.0 | 6.0 | 8.0 | 10.0 | 12.0 | 14.0
 | 1336277.6427 | 1341897.8391 | 1345975.5556 | 1351111.1276 | 1357427.5195 | 1362662.548 | 1370156.1432 | 1371794.463 | 1377640.6969 | 1382808.8183 | 1385770.8137 | 1390683.9648 | 1390772.5715 | 1392817.7588 | 1393463.3219 | 1390738.2138
Chart: z-position [micrometer]
| -11.25 | -10.0 | -8.75 | -7.5 | -6.25 | -5.0 | -3.75 | -2.5 | -1.25 | 0.0 | 1.25 | 2.5 | 3.75 | 5.0 | 6.25 | 7.5 | 8.75 | 10.0 | 11.25 | 12.5
 | 9031.007 | 10268.3705 | 12240.6285 | 16390.7 | 25625.919 | 45363.2775 | 98978.332 | 188709.3535 | 267858.969 | 291687.285 | 321612.404 | 275648.582 | 136471.3865 | 34882.634 | 14806.7135 | 9600.651 | 7351.632 | 5523.1285 | 4575.961 | 3619.389

## Slide 82
Scatter

## Slide 83
> "Performing Image QC:"
> "Measurement: ImageQuality_PowerLogLogSlope_DNA
> " Allowed range: -2.4 .. 100 and not NA.“
> " Images total: 69072"
> " Images failed: 485”

## Slide 84
Sample preparation
Microscopy
Sub-optimal type of microscopy
Sub-optimal filter settings
Saturated signals
Images saved in wrong format
Staining not sufficient or missing to segment all objects of interest (e.g. cellular cytoplasm)
Transfection efficiency too low
Staining did not work
Cell density too high or low
Cells mounting
Image Analysis
Statistics
Sub-optimal object segmentation
No significant difference between positive and negative controls
Staining “gradients”
Cell density “gradients”
Notes: The actual image analysis part is small and often not the actual challenge.
ASK for more ideas (Faba…)

## Slide 85
Image-based watershed using nuclei as “seeds”
You need a cytoplasm staining
You have to set the background threshold
Accurate at cell boundaries and cell-cell contacts

## Slide 86: Watershed on image gradient (maybe try for membrane staining…)

## Slide 87: Detailed Outline
Image analysis software
Data organisation
Object detection
  Intensity threshold
  Image filtering to enhance objects of interest
    Top-hat filter
    Difference of Gaussian filter
    Supervised pixel classification
Object splitting
Object dilation (region growing)
  Distance based
  Watershed
Object measurements
  Intensity
  Shape
  Texture
  Classification
Quantitative intensity measurements
  Interpretation depending on microscopy method
  Background subtraction
Automated quality control (filtering)
  Object-based
  Image-based

## Slide 88
Typical image QCs:
Focus quality > ?
Background intensity < ?
? < Cell density < ?